## Slide 1: Final Project
USPAS
Control Room Accelerator Physics
Albuquerque, New Mexico
June 17 - 28, 2019
SNS CCL Orbit Correction
Michelle Miller
Alyssa Miller
Trudy Bolin
Salvador Sosa

## Slide 2
CCL (coupled-cell linac) Orbit Correction
Orbit correction is a classical task for almost every accelerator.
Statement of Problem
  Create a script that will correct the vertical orbit in the CCL section of the SNS accelerator
  The script will communicate through EPICS with the OpenXAL Virtual Accelerator for the DTL6-CCL1-CCL2-CCL3-CCL4 subsequence. The orbit distortion will be created by one of the dipole correctors in DTL6
  Correct the orbit without using the OpenXAL online model
  By using the virtual accelerator, measure the response of all CCL BPMs to all vertical dipole correctors (DCV) and create a response matrix
  Solve the optimization problem by minimizing the vertical orbit deviation at the BPMs’ position by applying limited kicks from correctors
  Note: In CCL the DCV magnetic field is limited to 0.012 T

## Slide 3
Make a script start a virtual accelerator
Create a 2D array for kicks and BPM positions
Introduce kick to upstream dipole corrector (store in array)
Record all BPM’s (store in array)
Introduce another kick to downstream dipole corrector (store)
Again record all BPM’s
Go to next step
Introduce kick at a given dipole corrector
Look at all BPM’s and and fix
Go to next dipole corrector and introduce kick
Look at all BPM’s and fix
And so on
Create a response matrix
Algorithm
Go to next step
Invert response matrix
Results are used to provide the correction kicks
given the BPM readbacks
This will be used to correct any random error
Kicks
Response Matrix
Correction
Scan of the BPMs from the Virtual Accelerator
Optimization done offline

## Slide 4: SNS Linac
1000 MeV
Ion Source
RFQ
2.5 MeV
87 MeV
CCL
SRF, b=0.61
SRF, b=0.81
186 MeV
387 MeV
DTL
MEBT
To RING
RF
cavities
4 cav.
6 cav.
4 cav.
33 cav.
48 cav.
Warm (normal temperature)
linac
Cold (superconducting)
Linac (SCL)
Orbit distortion in DTL6
Orbit distortion in DTL6
Orbit correction in DTL6

## Slide 5: Response Matrix
Initial BPM readings.
Algorithm
Minimize orbit distortion by changing correctors
BPM
DCV
10 BPM’s
18 Dipole Correctors

## Slide 7: Results

## Slide 8: Ideal and Perturbed Orbits